## Slide 1: CO249 Risk Register is found by the entry Doors, please read and familiarise yourself with the Risks and Controls required in this Room
Risks in this Room
  Small Parts
  Electrical Equipment
  Lithium Batteries
  Soldering Irons
  Open Circuit boards
General Lab Rules for this Lab
  No Food or drink to be consumed in the room
  Required School supplied PPE must be worn
  Work must not be carried out without the correct PPE
  If you need PPE or think that it is not correct for the task - discuss with Supervisor, Technicians, H&S Rep
  Work must be carried out in the appropriate areas
  Report incidents/accidents
  Report all broken equipment/Desks/chairs
  Covered Footwear at all times- no jandals or bare feet permitted

## Slide 2: Lab Briefing
SAFETY PROCEDURES:
Soldering:
Risks:
Soldering iron tips are hot - up to 300 degrees. Never touch tip of the iron – remember, hot soldering iron looks exactly same as cold one. To check the temperature touch wet cleaning sponge at soldering stand with tip of the iron. If you can hear hissing sound – iron is hot enough to use.
Lead is hot as well and it does not stick to iron tip. Never shake soldering iron to remove excessive lead – always use cleaning sponge.

## Slide 3: Lab Briefing
Open Circuit Boards:
Risks:
These is a risk that open Printed Circuit Boards (PCB) carry or contain high voltages (voltages about 60V DC). Do not touch boards that are not yours. If you working on a PCB that has voltages greater than 60V DC on it, then their must signs warning of high voltages placed on or near it if you step away from it. Any work on PCB’s or equipment with voltages greater than 60V DC need to be cleared with the Technicians before work commences and before its plugged into a 240V power point.
Small Items:
Risks:
Small items may fall onto the floor while work is being carried out. These items may contain sharp edges or points which may embed into skin if enough force is present. Covered shoes must be warn to prevent this from happening. Please be aware that the Cleaners do not clean labs and so while it may look clean there will be small parts on the floor. The floors may be cleaned once a year, when there is the least disruption to occupants.

## Slide 4: Lab Briefing
Power supplies:
Risks:
We use Lithium batteries which potentially can explode when overheated or punctured. If you shorted the power supply board and see smoke or it smells of burning plastic – step away at once. Ask for lab supervisor attention same moment. Window of opportunity to stop battery from overheating is tens of seconds – do not try to cover your mishap.
If you dropped the battery – ask for replacement from Technicians.
Hand Tools:
Risks:
Tools can be sharp. If you cut yourself, see one of the Technicians for first aid.
When using battery drill ensure workpiece is safely secured such that the workpiece will not fly off.
Ensure the tool you are using is appropriate for the task you are wanting to do. If you are unsure ask a Technician.
Correct PPE must be worn. Minimum is covered shoes, however Safety Glasses and/or gloves maybe required.